# CAT #FF Series

# FLOOR POCKETS (FF)

Specifications:

The floor pocket shall be a wiring device designed for flush mount installation in the stage floor.  The floor pocket plate shall be constructed of cast aluminum with non-skid tread pattern and cable notches.  The plate shall contain four recessed mounting holes to secure plate to back box.  The cover shall be constructed with integral hinges and cable notches.  Secured to the plate shall be an angled sheet steel mounting plate for receptacles.  The back box shall be constructed of code gauge steel and shall be sized according to the number of connectors required.  Knockouts shall be provided in the back box for contractor connection.  The floor pocket shall meet the National Electrical Code requirements for installation in concrete.  The finish shall be baked black enamel.

The floor pocket shall be U.L. Listed and labeled.  Unit shall have a New York City Calendar Number.